## Slide 1: Arduino and Robots in the Classroom
Resources for Mentors and Teachers (updated for 2019)
Copyright 2020 Dan McCreary - Moving Rainbow Labs
Creative Commons Sharealike with Attribution for Noncommercial
Notes: https://creativecommons.org/licenses/by-sa/2.5/

## Slide 2: License Agreement
Creative Commons Licensed - Attribution NonCommercial ShareAlike 4.0
As a noncommercial organization, you are free to use and remix this content
Attribution is always appreciated
Use is limited for non-commercial purposes
Link to License Agreement

## Slide 3: Overview
What is Arduino?
Why is it so popular?
How to engage students
When to use Arduino in learning (and not use Arduino)
Basic circuits, breadboarding and components
Arduino displays and sensors
Challenges - downloading and drivers
Working with Arduino volunteers
Arduino kits - pre, basic, alternatives, advanced

## Slide 4: What is Arduino?
The de facto-standard for teaching physical computing
Physical Computing is a creative framework for understanding human beings' relationship to the digital world.
https://en.wikipedia.org/wiki/Physical_computing

## Slide 5: Arduino vs. 3D Printing vs. PIC microcontroller
Arduino
PIC Microcontroller
3D Printing

## Slide 6: Four Drivers
Maker Movement
Project-Based Learning
Low-Cost Components*
Social Media
"How to" sites
* If you know where to look

## Slide 7: What's New in 2019?
New version of the Arduino IDE
1.8.8 - more features and support for additional processors
New version of Arduino run-time libraries
Requires an additional step to use old run-time libraries
If you have a Nano with the old bootloader you must select
Tools > Processor > ATmega328P (Old Bootloader) to upload.
Lower Cost LED Strips and fantastic OLED DIsplays
$4.30 per meter (60 LEDS per meter)
Many new hardware devices
Low cost ESP-32 replacing the older Uno and Nano
Almost all of the more powerful and more expensive than the Arduino Nano

## Slide 8: Blue Ringed Octopus
Fantastic Costumes with longer strands of LEDs!
$4.30 per meter!

## Slide 9: Robot Day at The Works
"Hands-on" for kids 5 to 12 years
Notes: https://www.youtube.com/watch?list=PLmXh30-EMTVtWAIGz_7pImSKRsJ_z8Yn1&v=pZHZEA6dJro

## Slide 10: Donkey Car Movement
2,500 members in Oakland CA
Hundreds of people at a events racing their "AI" cars

## Slide 11: FaceBot and Amazon Deep Racer
$37
$399
$249

## Slide 12: ESP-32 and Pi Zero
512K RAM (Compare with Arduino Uno at 2K)
Built in WiFi and Bluetooth
Use Arduino IDE to program
$6
512K RAM
Built in WiFi and Bluetooth
Linux OS
$20

## Slide 13: More Displays - easier to use!
LED (1 cent)
2.8" TFT 128 x 160 ($9)
0.96" OLED 128 x 64 with 2 wire I2C interface ($3.50)
8-digit 7 segment displays ($3)
7 Segment display (20 cents)
10 segment bars ($1.20)
Addressable RGB LED Strip 60 per meter ($10/meter)
16x2 Backlit LCD with 2-wire I2C ($1.49)
Nokia 5110 LCD 84x48 ($4)

## Slide 14: Larger Arduino Displays
Lower cost, more colors, higher resolution, easier to connect with fewer wires
https://www.youtube.com/watch?v=E6quVf1_BIg

## Slide 15: 2.42 inch monochorme 128x64 OLEDs for $17

## Slide 16: 2.24 OLED Screen
Very high contrast
Low power
Easy to program with the u8l2 library
Five pins (plus GND and +5V)

## Slide 17: Color OLED 160x120 $21 from Digole
Special serial software to make drawing fast

## Slide 18: $37 Facebot
64x128 OLED display
Bright, high contrast, large viewing angles
Adds $12 to the price of the base CoderDojo robot

## Slide 19: Strategy
Focus on making the first five labs fun
Focus on engaging students and identifying their interests
Most students that get through the first labs without frustrations go on to do more on their own
Pay careful attention to all the details of the first few labs
Once students have foundational knowledge they can "Google" for ideas and solutions
Partner projects with 2-hours of mentoring every other week

## Slide 20: 1.82 2.6 Million Arduino Videos on YouTube
Huge repository of learning
Everything from basic usage to advanced topics
Students love to show their projects

## Slide 21: Teaching and Arduino in Practice
A software development platform with associated standard chips
An open platform for makers to build things
A framework for teaching physical computing, electronics and computer science
A system for building rapid prototypes in industry
A place where we can find trained volunteers!

## Slide 22: Keys to Involvement
Use Color!
Use Motion!
Affordable kits (under $15) that can be taken home
Get students to work in teams
Encouraging their own ideas
Students become the best "sales people" (show and tell)
Leverage a growing community of volunteers
The "right" amount of parental involvement

## Slide 23: Fitting to Learning Objectives
Physics
Conductivity, voltage, current, power, batteries
Computer Science
Loops, variables, datatypes, conditionals
Art and Costume Design
Color, patterns, sensors, interactivity, wearability
Robotics
Motors, servos, sensors, control theory,

## Slide 24: Knowledge Foundations
Breadboarding
Computer Science
Arduino IDE
Basic Electronics
Arduino Projects
Sensors
Displays
Arduino Functions

## Slide 25: Challenges
Complexity
What do we need to know before we add Arduino to our classroom?
What happens if there is a problem I can't fix?
What goals are realistic?
Laptops
Arduino IDE
USB Drivers
Arduino Libraries

## Slide 26: Learning Paths
It all starts with "blink"
LED Blink Lab
Sensors
Displays
Motors
Servos
Light
Sound
Buttons
Knobs
LED
strips
arrays
LCD
OLED
Speakers
Stepper
Halloween Costumes
Temp
Robots
Controllers
Use Headsets
in Classroom
Exotic Sensors
RC-Copter
Touch
Flex

## Slide 27: The Arduino Desktop Software
Integrated Development Environment (IDE)
Allows editing, compiling, uploading and monitoring all is one package
Good experience for any future software developer
Learn compile, upload, new, open save and serial monitor
Load examples into your Arduino Home/libraries

## Slide 28: Genuine Arduino vs. Arduino Clones on eBay
Option 1: Genuine Arduino From Italy - $29.95 + $3.74 Shipping
Option 2: Arduino Nano Clone from on eBay
$2.29 (free shipping, two weeks delivery from China)
Breadboard friendly but needs a special CH340D driver
http://store-usa.arduino.cc/products/a000066

## Slide 29: Teaching Breadboarding Skills
Vertical power rails and horizontal row connectors
Available on e-bay for $1.20 each qty 1
Good overview at: https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard
400 Tie Medium Breadboard with power rails

## Slide 30: Name the parts
Power Rails
Columns
(Bus Strips)
Component Slot
Red for +5 V
Blue (Black) for GND
Row connectors

## Slide 31: Start Slowly - Breadboard Lab
Ask: Have you ever used a solderless breadboard before?
Plug in the Arduino to the USB serial port. Note the power light. Unplug and re-plug the USB to reinforce that the power is coming from the PC
Connect the power (+5) and ground (GND) using jumpers
Plug the motor pins into one of the power rails - note the change in direction when you reverse the connectors

## Slide 32: LED Lab
Put an LED in the center of the breadboard and note the long side (cathode)
Add a 330 Ohm resistor
Connect the long wire Anode to +5 and the resistor to GND
https://learn.sparkfun.com/tutorials/polarity/diode-and-led-polarity
Anode - the positive (+) side is longer and sometimes has a bend in the wire
Cathode - the negative (-) or ground side is shorter and is connected to the black rail
-
+

## Slide 33: Cathode and Anode
My tall friend Ann who loves red! The long positive side.
My short black cat. The short ground (negative) side.

## Slide 34: LED Circuit
Basic Red LED Circuit
The resistor limits the current to around 10 mA
Use this circuit to test the breadboard
Note that you will burn out the LED if you omit the resistor!
Red LEDs have a voltage drop of about 1.8 volts
LEDs cost about 1.2 cents each
Arduino +5 V
or output pin
Anode
Cathode
330 Ohm
Resistor
GND
or
3 AA Batteries
3.2v

## Slide 35: A great time to practice a bit of math...
Ohm's Law:
I = E / R
Current = Voltage / Resistance
Voltage = 5 Volts - Diode Voltage Drop (1.8 for red) = 3.2 volts
Resistance = 330 Ohms
Current = 3.2 / 330 ~ 0.010 Amps or 10 milliamps
LEDs burn out if the current goes over 20 milliamps
Each full circuit is an equation and the current at any point is the same
Google "LED resistor calculator"
Current =
Voltage
Restance

## Slide 36: Resistor Codes
330 Ohm

## Slide 37: LED Circuit on the breadboard
+5 to power rail
GND to other side
Resistor to one row
LED across the middle
No Arduino required!

## Slide 38: Button Lab
Connect LEDs and resistors in series to momentary push buttons.
Create AND/OR logic circuits
$3/kit
No need for an arduino or laptop

## Slide 39: 100pcs Ultra Bright Red LED = $1.19 with shipping

## Slide 40: Lab #1: Blink Lab
Replace +5 with power from pin 13

## Slide 41: Sample Blink Engagement and Extension Questions
Can you change the speed of how fast it flashes?
What is delay(1000); doing?
What is half of 1000? What does delay(500) do?
Can you make it stay on for twice the time it is off?
Can you make it flash like a heartbeat? (short on, long off)
How fast can you make it flash and still see it flickering?
Do you think that the limits are with the LED or your eye?
Did you know that fluorescent lights do the same thing?
Can you make it flash twice fast and then pause for 2 seconds?
Can you make a second LED flash?
Can you alternate flashing on two LEDs?
Can you make three LEDs flash one after the other?
void loop() {
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delay(1000);
}
Get them to re-upload a test program at least 10 times….
Incremental complexity

## Slide 42: Potentiometer
Ends of the potentiometer are wired to 5+ and GND
The voltage at the center tap will range from GND to +5v as the knob is turned
The center tap goes to the Arduino port A0
+5V
GND
Center Tap

## Slide 43: Lab 2: Reading a POT with AnalogRead()
The speed of the LED will change based on the value of the potentiometer

## Slide 44: Read Sensor
int sensorPin = A0; // select the input pin for the potentiometer
int ledPin = 13; // select the pin for the LED
int sensorValue = 0; // variable to store the value coming from the sensor
void setup() {
// declare the ledPin as an OUTPUT:
pinMode(ledPin, OUTPUT);
}
void loop() {
// read the value from the sensor:
sensorValue = analogRead(sensorPin);
// turn the ledPin on
digitalWrite(ledPin, HIGH);
// stop the program for <sensorValue> milliseconds:
delay(sensorValue);
// turn the ledPin off:
digitalWrite(ledPin, LOW);
// stop the program for for <sensorValue> milliseconds:
delay(sensorValue);
}
Note use of variables for pin numbers
The value of the sensor (0-1023) will change the delay from 0 to just over one second
Exercise, use the map() function to make the delay vary from 20 to 3 seconds
delay = map(sensorValue, 0, 1024, 20, 3000)

## Slide 45: BookMark the "SparkFun Experiment Guide for Arduino"
https://learn.sparkfun.com/tutorials/sik-experiment-guide-for-arduino---v32/

## Slide 46: Lab 3: Driving RGB LEDs
RGB Clear Common Cathode LED
Quick - what side is the "Cathode"?
Longest leg goes to ground
Resistors to each other leg
GND
Pin 11
Pin 10
Pin 9

## Slide 47: Pulse Width Modulation (PWM)
Using digital HIGH and LOW to simulate an analog value
See analogWrite() https://www.arduino.cc/en/Reference/AnalogWrite

## Slide 48: Note the "~" next to pins 11, 10, 9, 6, 5 and 3
Not all output pins support PWM!

## Slide 49: Each pin controls one color (R, G and B)
Wire long pin to GND
Wire other pins through resistors to Arduino PWM pins 9, 10 and 11
Load "Circuit 3" in SparkFun inventor's kit
https://learn.sparkfun.com/tutorials/sik-experiment-guide-for-arduino---v32/experiment-3-driving-an-rgb-led

## Slide 50: Lab 4: Row of Multiple LEDs
First use of complex data structure (Array of LED pins)
int ledPins[] = {2,3,4,5,6,7,8,9};
First use of "for" loop
Many ways to modify for different patterns!
Well worth the time to wire

## Slide 51: Sample for Loop
for(index = 0; index <= 7; index++) { pinMode(ledPins[index],OUTPUT); // ledPins[index] is replaced by the value in the array. // For example, ledPins[0] is 2 }
start
exit condition
increment by one

## Slide 52: Lab #5: Push Buttons
Use of momentary switch
Analog vs. Digital
Variables
Conditions!

## Slide 53: Push Button Code Setup
Note the use of variables for the pin numbers
const int button1Pin = 2; // pushbutton 1 pin const int button2Pin = 3; // pushbutton 2 pin const int ledPin = 13; // LED pin
void setup() { // Set up the pushbutton pins to be an input: pinMode(button1Pin, INPUT); pinMode(button2Pin, INPUT); // Set up the LED pin to be an output: pinMode(ledPin, OUTPUT); }

## Slide 54: Conditional IF/THEN/ELSE Logic
if (((button1State == LOW) || (button2State == LOW)) // if we're pushing button 1 OR button 2 && ! // AND we're NOT ((button1State == LOW) && (button2State == LOW))) // pushing BOTH button 1 AND button 2 // then... { digitalWrite(ledPin, HIGH); // turn the LED on } else { digitalWrite(ledPin, LOW); // turn the LED off }
Where is the "Then" Statement? Missing! It is implied after the IF statement

## Slide 55: Lab 7: Reading a digital temperature sensor
Analog sensor that sends a voltage that depends on temperature
Use of conversion function
First use of a subroutine function
First use of the printing to the serial monitor
Temperature sensors are very small and easy to lose

## Slide 56: Main Loop with Printing
Same analogRead() as POT lab
Use of float data type
Use of math equations
Use of conversion to units
void loop() { float voltage, degreesC, degreesF; voltage = getVoltage(temperaturePin); degreesC = (voltage - 0.5) * 100.0; degreesF = degreesC * (9.0/5.0) + 32.0; Serial.print("voltage: "); Serial.print(voltage); Serial.print(" deg C: "); Serial.print(degreesC); Serial.print(" deg F: "); Serial.println(degreesF); delay(1000);}
float getVoltage(int pin) { return (analogRead(pin) * 0.004882814);}

## Slide 57: Lab 8: Servos
Change the angle of the arm of a servo
Students LOVE motion!
Change the angle of the servo arm in loop (0, 90, 180 degrees)
First use of a library!
#include <Servo.h> // servo library
servo1.attach(9);
servo1.write(180);

## Slide 58: Lab 9: Flex Sensor
Builds on Lab 8
Change the angle of a servo arm based on how much the flex sensor is bending
Favorite lab of many students
Gets them to think about remote robot control

## Slide 59: Lab 10: Reading a Soft Pot
Change the color of the RGB LED based on where you touch the sensor
Pins on soft pot are easily bent
Note the 10K pull-down resistor from the middle pin to ground!
Note 10K pull-down resistor (not 330 Ohm)

## Slide 60: Other Labs in SIK V 3.2
11 Buzzer (avoid in large classrooms)
12 Relay (hard to use in breadboards)
13 Shift Register (many wires)
14 Motor (small transistors and diodes)
15 LCD display (a favorite but many wires)
16 Simon Game (not included in our kits)

## Slide 61: Moving on...
build a computer from components
breadboards can get complex...but the skills they learn now might help in college!

## Slide 62: Arduino Nano on a breadboard
Many "kits" start with a low cost Arduino Nano on a breadboard.
Easy to extend.
Short wires to power and ground.

## Slide 63: Sensors
Using AnalogRead() function to read values from 0 to 1023
https://www.arduino.cc/en/Reference/AnalogRead
Use map function to convert values into other ranges
newValue = map(inputValue, inLow, inHigh, outLow, outHigh)
Reads the value from the specified analog pin. The Arduino board contains a 6 channel (8 channels on the Mini and Nano, 16 on the Mega), 10-bit analog to digital converter. This means that it will map input voltages between 0 and 5 volts into integer values between 0 and 1023.
analogRead()

## Slide 64: All the light we can not see (and sounds we cannot hear)
Encourage students to use sensors that sense "invisible" information
Infrared and Ultrasound

## Slide 65: Best Practice Sensors
PIR Motion Sensor (Passive Infrared)
$1.40
http://www.ebay.com/itm/HC-SR501-Adjust-IR-Pyroelectric-Infrared-PIR-Motion-Sensor-Detector-Module-NEW/271638488228
PING Sensor (Ultrasonic distance sensor)
$1.00
http://www.ebay.com/itm/1pcs-Ultrasonic-Module-HC-SR04-Distance-Measuring-Transducer-Sensor-for-Arduino-/171983646391

## Slide 66: Not all are real "sensors" but all can be fun
KY-001 Temperature sensor module
KY-002 Vibration switch module
KY-003 Hall magnetic sensor module
KY-004 Key switch module
KY-005 Infrared emission sensor module
KY-006 Small passive buzzer module
KY-008 Laser sensor module
KY-009 3-color full-color LED SMD modules
KY-010 Optical broken module
KY-011 2-color LED module
KY-012 Active buzzer module
KY-013 Temperature sensor module
KY-015 Temperature and humidity sensor module
KY-016 3-color LED module
KY-017 Mercury open optical module
KY-018 Photo resistor module
KY-019 5V relay module
KY-020 Tilt switch module
KY-021 Mini magnetic reed modules
KY-022 Infrared sensor receiver module
KY-023 XY-axis joystick module
KY-024 Linear magnetic Hall sensors
KY-025 Reed module
KY-026 Flame sensor module
KY-027 Magic light cup module
KY-028 Temperature sensor module
KY-029 Yin Yi 2-color LED module 3MM
KY-031 Sensor module
KY-032 Obstacle avoidance sensor module
KY-033 Hunt sensor module
KY-034 Automatic flashing colorful LED module
KY-035 Class Bihor magnetic sensor
KY-036 Metal touch sensor module
KY-037 Sensitive microphone sensor module
KY-038 Microphone sound sensor module
KY-039 Detect the heartbeat module
KY-040 Rotary encoder module

## Slide 67: Success Stories
LED Costume Kit ($13.5)
Done with the Internet of Things Hackfest
LED Strip Box (Moving Rainbow)
Motor Controllers
Simple kit to move a motor forward and reverse
CoderDojo Robot
Done as advanced projects for CoderDojo students

## Slide 68: Sample Beginner Projects
Nightlight (photosensor and LED)
Room Alarm (PIR sensor and buzzer)
Temperature display and alarm
Tilt sensor and alarm
Simple Simon pattern replay game (4 push buttons, LEDs and optional speaker)
Motor controller

## Slide 69: Challenges
PC Can't Connect to the Arduino
(Upload will not work)
Drivers not installing
Mac unsigned drivers
Programs will not compile
Syntax errors

## Slide 70: Windows Device Manager
Note COM23 is the port

## Slide 71: Problem uploading to board
Note the Processor and Port

## Slide 72: Checking the USB on The Mac
About This Mac…
System Report…
USB

## Slide 73: Note the port when you plug in the Arduino

## Slide 74: Low Cost Arduino Nano Using the CH340
Note that the CH340 is the name of the USB serial interface chip, not the actual Arduino processor.
The driver comes from wch.cn

## Slide 75: Problem: The Rote Learner Problem
Students carefully follow the detailed steps in SparkFun inventor's kit guide
Each wire is carefully connected and checked
Each lab "works"
Students have little understanding of what is really going on and can't build their own projects

## Slide 76: Tip for Teaching New Students
Make the font-size larger for new students (Arduino -> Preferences)
Remove comments when doing code-walk-throughs
Restart the Arduino software after a resize

## Slide 77: Key Computer Science Topics
Variables
Loops (for loops)
Conditional statements (if/then/else)
Data types (integer, float, bytes)
Data range conversions

## Slide 78: Teach debugging
Learn how to add "print" statements
Open the serial monitor

## Slide 79: Addressable LED Strips (WS2812B)
1 Meter @$14.24
60 RGB LEDs/meter
$4.60 per LED strip
Easy to connect
  Ground wire
  5V power wire
  data wire

## Slide 80: Moving Rainbow Labs
Focus on fun colors and patterns
Reinforce many Computer Science concepts (loops, conditionals)
Perfect for costumes and interactive art
Online book with instructor's guide
  http://moving-rainbow.readthedocs.org/en/latest/README/
Simple to connect
(three wires)

## Slide 81: Controlling Motors: The H-Bridge Circuit
Close Switch 1 and 4 for forward direction
Closes switch 2 and 3 for reverse direction
Never close S1 and S2 or S3 and S4 together (short circuit)

## Slide 82: Motor Driver Labs
Based on standard low cost two motor controller chip (L293D) 40 cents each
Goal - make two motors turn forward and backward
Basis for robot movement
Once students believe they can control two wheels they are ready to build a simple robot
Over 75% of students that finish the motor driver lab go on to build their own robot!
http://www.ebay.com/itm/10Pcs-L293D-L293-Push-Pull-Four-Channel-Motor-Driver-IC-/140832908826

## Slide 83: Simple hookup
Introduction to "PWM" for motor speed control
H-Bridge circuit
Direction control
Use a potentiometers to change the direction and speed of two motors.

## Slide 84: 12 Volt battery to pin 8
Pin 8
5 Volts

## Slide 85: CoderDojo Robot Labs
Collision avoidance robot
Designed as advanced labs for CoderDojo students
Students use kits at CoderDojo and then purchase their own for around $35
Totally open design
  3 breadboards on the top
  Easy to change and add sensors
Includes addressable strip
Uses Arduino Nano

## Slide 86: Keep the steps small
Don't add too much complexity too fast
Blink
Analog
Breadboarding
Uploading
Blink
Sensors
Bluetooth
Wireless
Internet of Things
Raspberry Pi
UNIX
Wifi LAB
Servo

## Slide 87: Arduino Kits
Pre-Arduino kits - breadboarding basics $5/kits
Basic Arduino kits - $25-$110 /kits
LED kits - $10 to $40
Robot kits - $40 to $300

## Slide 88: Sample Breadboard Kit
400 tie breadboard ($1.20)
Battery case or wall-transformer ($2-$4)
Jumpers (< $1)
10 Resistors (< 50 cents)
10 LEDs (< $1)
Optional Motor (< $2)
Optional Potentiometer (< $1)
No Arduino needed! No PC Needed!
Builds the foundation for all future Arduino labs
Help students build fine-motor skills
Easy to setup
Some soldering required for motors
Google: "Breadboard starter kit"
http://www.ebay.com/itm/BreadBoard-Starter-Kit-Power-Supply-Module-Resistors-Wires-more-/171924251290
Sample $25 Kit
http://www.ebay.com/itm/Electronics-fans-kit-for-arduino-starter-resistor-breadboard-LED-dupont-cable-/131650525657
Sample $10 Kit

## Slide 89: Sample $15 Kit
http://www.ebay.com/itm/Basic-Electronic-Component-Kits-Breadboard-Resistors-Power-Supply-Module-J0JF/141832343887
$15.00 US with shipping from China
Use to teach basics of breadboarding, power, conductivity, resistors, LEDs, potentiometers, and buttons
Excellent preparation for Arduino labs

## Slide 90: Sample item on e-Bay
Note to select "Buy It Now" and Sort by "Price + Shipping: lowest first"

## Slide 91: Breadboard vs. Little Bits
LEDs with resistors QTY 100 for $2.00 (2 cents each) but requires fine motor skills
Little Bits sells a Single LED for $10.00. Great for students that don't yet have fine motor skills...but does not teach breadboarding/debugging skills.

## Slide 92: SparkFun Inventor's Kit
Used in many CoderDojo labs
Many Arduino mentors now familiar with these kits
Good selection of parts and excellent printed guidebook
Redboard Version 3.2 list price is $99.00
  (Add $10 for Genuine Arduino from Italy)
No soldering required to use base kit
Soldering is used to reinforce and repair motors
Small parts moved to a separate bin

## Slide 93: SIK Guide and Case
SIK Guide and Case and reinforced cable ties on motors

## Slide 94: 16hertz Kits
Great value! $25.00
Requires 20 minutes of soldering for each kit
Larger servo, relay
Well written guide
http://www.16hertz.com/product/16hertz-uno-r3-beginner-kit-arduino-compatible/

## Slide 95: 37 Sensors Kit
http://www.ebay.com/itm/Pro-Compatible-37-in-1-Sensor-Modules-Kit-Arduino-Ultimate-MCU-User-Free-Case-/141772914818
37 Sensors for $27.00
Variety of devices (not all sensors) for under $1/device
Kit comes with no instructions and the contents frequently change
Many examples of how to use each device on the Internet
Remove any "mercury" switches

## Slide 96: Robot Kit
Open design
$35 in parts
Ping sensor on mini-breadboard to detect objects in front
Arduino Nano on a breadboard
LED strip
L293D Motor Driver
https://www.gitbook.com/book/dmccreary/coderdojo-robots/details

## Slide 97: Robots: mBot, MIP, Gizmo
Cozmo - $179.00
Coder MIP - $79.00
mBot - $99.00

## Slide 98: MicroCenter
Carry in-house brand Arduino for $9.99
Large selection of kits and sensors
2-3 times eBay "best prices"

## Slide 99: Encourage Volunteers
There are many parents that may have some programming or electrical knowledge
Find a parent or mentor to solder broken parts and put solid wire pins on components that are hard for small fingers
10 kits - no working motors
2 hours of soldering - 10 working motors
http://datadictionary.blogspot.com/2014/10/motors-for-arduino-labs.html

## Slide 100: Watch how students make "connections"
Have plenty of 22 gauge solid wire, jumper wires of various lengths
Add heat shrink around ends

## Slide 101: Mentors are critical for overcoming frustration
Problem
  Many kids hit "the wall" when they can't get a project to work
  New students can easily get frustrated and quit
  Parents purchase expensive Arduino kits and they go unused
The Solution: develop mentor programs
  Try CoderDojoTC (every other Saturday at the U of M)
  Keep students from thinking that Arduino is frustrating
  A good mentor will keep challenging the students

## Slide 102: Student / Book / Box / Mentor Relationship Analysis
Focus analysis on the six key relationships and the break/fix cycle
Student
Book or
Web Site
Robot/Kit
Teacher/Mentor

## Slide 103: Component/Libraries/Documentation/Sample Code
Where should we look for components? Have we used this component before? How many will we need for a classroom? Can I find other teachers that can help us get started?
Higher cost components with good documentation, libraries, examples and support. (Adafruit, Sparkfun)
Lower cost components with no documentation, no support and no sample code. (Amazon, e-Bay)

## Slide 104: Three Take-home Points
Always have a mentor
Studies show that spending two hours every other week keeps students on the STEM track
Ask students bring their ideas
The mentor's job is to find out how to make it happen
Work in teams to build concrete projects
"Social Constructionism" is perhaps the best way to learn both hard and soft skills

## Slide 105: Summary
Arduino is a foundation technology
Arduinos open many doors
Learning Arduino is great ways to help students become "makers" and become involved in project-based learning
Arduinos take time to master
Start simple
Purchase basic kits
Work with peers to help overcome problems
Come to CoderDojo to learn new things!

## Slide 106: Questions
Dan McCreary
dan.mccreary@gmail.com
https://github.com/dmccreary/moving-rainbow
https://github.com/dmccreary/coderdojo-robots
LinkedIn: https://www.linkedin.com/in/danmccreary/
Twitter: @dmccreary