## Slide 1: MicroPython and Robots in the Classroom
Resources for Mentors and Teachers (updated for 2023)
Copyright 2020 to 2023 Dan McCreary - Moving Rainbow Labs
Creative Commons Sharealike with Attribution for Noncommercial
Notes: https://creativecommons.org/licenses/by-sa/2.5/

## Slide 2: License Agreement
Creative Commons Licensed - Attribution NonCommercial ShareAlike 4.0
As a noncommercial organization, you are free to use and remix this content
Attribution is always appreciated
Use is limited for non-commercial purposes
Link to License Agreement

## Slide 3: Overview
What is MicroPython?
Why is it so popular?
How to engage students
When to use MicroPython in learning (and not use MicroPython)
Basic circuits, breadboarding and components
Displays and sensors
Challenges - downloading and drivers
Working with volunteers
Beginning Electronics kits - pre, basic, alternatives, advanced

## Slide 4: What is MicroPython?
A variation of Python, the most popular language for education
physical computing
Physical Computing is a creative framework for understanding human beings' relationship to the digital world.
https://en.wikipedia.org/wiki/Physical_computing

## Slide 5: Four Drivers Promoting MicroPython
Maker Movement
Project-Based Learning
Low-Cost Components*
Social Media
"How to" sites
* If you know where to look
MicroPython

## Slide 6: Blue Ringed Octopus
Fantastic Costumes with longer strands of LEDs!
$4.30 per meter!

## Slide 7: Robot Day at “The Works Museum”
"Hands-on" for kids 5 to 12 years
Notes: https://www.youtube.com/watch?list=PLmXh30-EMTVtWAIGz_7pImSKRsJ_z8Yn1&v=pZHZEA6dJro

## Slide 8: Donkey Car Movement
2,500 members in Oakland CA
Hundreds of people at a events racing their "AI" cars

## Slide 9: FaceBot and Amazon Deep Racer
$37
$399
$249

## Slide 10: ESP-32 and Pi Zero
512K RAM (Compare with Arduino Uno at 2K)
Built in WiFi and Bluetooth
Use Arduino IDE to program
$6
512K RAM
Built in WiFi and Bluetooth
Linux OS
$20

## Slide 11: More Displays - easier to use!
LED (1 cent)
2.8" TFT 128 x 160 ($9)
0.96" OLED 128 x 64 with 2 wire I2C interface ($3.50)
8-digit 7 segment displays ($3)
7 Segment display (20 cents)
10 segment bars ($1.20)
Addressable RGB LED Strip 60 per meter ($10/meter)
16x2 Backlit LCD with 2-wire I2C ($1.49)
Nokia 5110 LCD 84x48 ($4)

## Slide 12: Larger Arduino Displays
Lower cost, more colors, higher resolution, easier to connect with fewer wires
https://www.youtube.com/watch?v=E6quVf1_BIg

## Slide 13: 2.42 inch monochorme 128x64 OLEDs for $17

## Slide 14: 2.24 OLED Screen
Very high contrast
Low power
Easy to program with the u8l2 library
Five pins (plus GND and +5V)

## Slide 15: Color OLED 160x120 $21 from Digole
Special serial software to make drawing fast

## Slide 16: $37 Facebot
64x128 OLED display
Bright, high contrast, large viewing angles
Adds $12 to the price of the base CoderDojo robot

## Slide 17: Strategy
Focus on making the first five labs fun
Focus on engaging students and identifying their interests
Most students that get through the first labs without frustrations go on to do more on their own
Pay careful attention to all the details of the first few labs
Once students have foundational knowledge they can "Google" for ideas and solutions
Partner projects with 2-hours of mentoring every other week

## Slide 18: 11 million results on Google
Huge repository of learning
Everything from basic usage to advanced topics
Students love to show their projects

## Slide 19: Teaching and MicroPython in Practice
A software development platform with associated standard chips
An open platform for makers to build things
A framework for teaching physical computing, electronics and computer science
A system for building rapid prototypes in industry
A place where we can find trained volunteers!

## Slide 20: Keys to Involvement
Use Color!
Use Motion!
Affordable kits (under $15) that can be taken home
Get students to work in teams
Encouraging their own ideas
Students become the best "sales people" (show and tell)
Leverage a growing community of volunteers
The "right" amount of parental involvement

## Slide 21: Fitting to Learning Objectives
Physics
Conductivity, voltage, current, power, batteries
Computer Science
Loops, variables, datatypes, conditionals
Art and Costume Design
Color, patterns, sensors, interactivity, wearability
Robotics
Motors, servos, sensors, control theory,

## Slide 22: Knowledge Foundations
Breadboarding
Computer Science
Arduino IDE
Basic Electronics
MicroPython Projects
Sensors
Displays
Arduino Functions

## Slide 23: Challenges
Complexity
What do we need to know before we add MicroPython to our classroom?
What happens if there is a problem I can't fix?
What goals are realistic?
Laptops
Thonny IDE
MicroPython Libraries

## Slide 24: Learning Paths
It all starts with "blink"
LED Blink Lab
Sensors
Displays
Motors
Servos
Light
Sound
Buttons
Knobs
LED
strips
arrays
LCD
OLED
Speakers
Stepper
Halloween Costumes
Temp
Robots
Controllers
Use Headsets
in Classroom
Exotic Sensors
RC-Copter
Touch
Flex

## Slide 25: The Thonny Desktop Software
Integrated Development Environment (IDE)
Allows editing, compiling, uploading and monitoring all is one package
Good experience for any future software developer
Learn compile, upload, new, open save and serial monitor
Load examples into your Raspberry Pi Pico

## Slide 26: Raspberry Pi Pico
Option 1: $4 without headers or wireless
Option 2: $5 with headers
Option 3: $6 with wireless (WiFi and Bluetooth)
Pico
Pico-W

## Slide 27: Teaching Breadboarding Skills
Vertical power rails and horizontal row connectors
Available on e-bay for $1.20 each qty 1
Good overview at: https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard
400 Tie Medium Breadboard with power rails

## Slide 28: Name the parts
Power Rails
Columns
(Bus Strips)
Divider
Red for power
Blue (Black) for GND
Row connectors
Terminal Strips

## Slide 29: Start Slowly - Breadboard Lab
Ask: Have you ever used a solderless breadboard before?
Plug in the Arduino to the USB serial port. Note the power light. Unplug and re-plug the USB to reinforce that the power is coming from the PC
Connect the power (+5) and ground (GND) using jumpers
Plug the motor pins into one of the power rails - note the change in direction when you reverse the connectors

## Slide 30: LED Lab
Put an LED in the center of the breadboard and note the long side (cathode)
Add a 330 Ohm resistor
Connect the long wire Anode to +5 and the resistor to GND
https://learn.sparkfun.com/tutorials/polarity/diode-and-led-polarity
Anode - the positive (+) side is longer and sometimes has a bend in the wire
Cathode - the negative (-) or ground side is shorter and is connected to the black rail
-
+

## Slide 31: Cathode and Anode
My tall friend Ann who loves red! The long positive side.
My short black cat. The short ground (negative) side.

## Slide 32: LED Circuit
Basic Red LED Circuit
The resistor limits the current to around 10 mA
Use this circuit to test the breadboard
Note that you will burn out the LED if you omit the resistor!
Red LEDs have a voltage drop of about 1.8 volts
LEDs cost about 1.2 cents each
Arduino +5 V
or output pin
Anode
Cathode
330 Ohm
Resistor
GND
or
3 AA Batteries
3.2v

## Slide 33: A great time to practice a bit of math...
Ohm's Law:
I = E / R
Current = Voltage / Resistance
Voltage = 5 Volts - Diode Voltage Drop (1.8 for red) = 3.2 volts
Resistance = 330 Ohms
Current = 3.2 / 330 ~ 0.010 Amps or 10 milliamps
LEDs burn out if the current goes over 20 milliamps
Each full circuit is an equation and the current at any point is the same
Google "LED resistor calculator"
Current =
Voltage
Restance

## Slide 34: Resistor Codes
330 Ohm

## Slide 35: LED Circuit on the breadboard
+5 to power rail
GND to other side
Resistor to one row
LED across the middle
No Arduino required!

## Slide 36: Button Lab
Connect LEDs and resistors in series to momentary push buttons.
Create AND/OR logic circuits
$3/kit
No need for an arduino or laptop

## Slide 37: 100pcs Ultra Bright Red LED = $1.19 with shipping

## Slide 38: Lab #1: Blink Lab
Replace +5 with power from pin 13

## Slide 39: Sample Blink Engagement and Extension Questions
Can you change the speed of how fast it flashes?
What is delay(1000); doing?
What is half of 1000? What does delay(500) do?
Can you make it stay on for twice the time it is off?
Can you make it flash like a heartbeat? (short on, long off)
How fast can you make it flash and still see it flickering?
Do you think that the limits are with the LED or your eye?
Did you know that fluorescent lights do the same thing?
Can you make it flash twice fast and then pause for 2 seconds?
Can you make a second LED flash?
Can you alternate flashing on two LEDs?
Can you make three LEDs flash one after the other?
void loop() {
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delay(1000);
}
Get them to re-upload a test program at least 10 times….
Incremental complexity

## Slide 40: Potentiometer
Ends of the potentiometer are wired to 5+ and GND
The voltage at the center tap will range from GND to +5v as the knob is turned
The center tap goes to the Arduino port A0
+5V
GND
Center Tap

## Slide 41: Lab 2: Reading a POT with AnalogRead()
The speed of the LED will change based on the value of the potentiometer

## Slide 42: Read Sensor
Note use of variables for pin numbers
The value of the sensor (0-1023) will change the delay from 0 to just over one second
Exercise, use the map() function to make the delay vary from 20 to 3 seconds
delay = map(sensorValue, 0, 1024, 20, 3000)

## Slide 43: Lab 3: Driving RGB LEDs
RGB Clear Common Cathode LED
Quick - what side is the "Cathode"?
Longest leg goes to ground
Resistors to each other leg
GND
Pin 11
Pin 10
Pin 9

## Slide 44: Pulse Width Modulation (PWM)
Using digital HIGH and LOW to simulate an analog value
See analogWrite() https://www.arduino.cc/en/Reference/AnalogWrite

## Slide 45: Sample for Loop
start
exit condition
increment by one

## Slide 46: Lab #5: Push Buttons
Use of momentary switch
Analog vs. Digital
Variables
Conditions!

## Slide 47: Push Button Code Setup
Note the use of variables for the pin numbers

## Slide 48: Conditional IF/THEN/ELSE Logic
Where is the "Then" Statement? Missing! It is implied after the IF statement

## Slide 49: Lab 7: Reading a digital temperature sensor
Analog sensor that sends a voltage that depends on temperature
Use of conversion function
First use of a subroutine function
First use of the printing to the serial monitor
Temperature sensors are very small and easy to lose

## Slide 50: Main Loop with Printing
Same analogRead() as POT lab
Use of float data type
Use of math equations
Use of conversion to units

## Slide 51: Lab 8: Servos
Change the angle of the arm of a servo
Students LOVE motion!
Change the angle of the servo arm in loop (0, 90, 180 degrees)
First use of a library!
#include <Servo.h> // servo library
servo1.attach(9);
servo1.write(180);

## Slide 52: Lab 9: Flex Sensor
Builds on Lab 8
Change the angle of a servo arm based on how much the flex sensor is bending
Favorite lab of many students
Gets them to think about remote robot control

## Slide 53: Lab 10: Reading a Soft Pot
Change the color of the RGB LED based on where you touch the sensor
Pins on soft pot are easily bent
Note the 10K pull-down resistor from the middle pin to ground!
Note 10K pull-down resistor (not 330 Ohm)

## Slide 54: Other Labs in SIK V 3.2
11 Buzzer (avoid in large classrooms)
12 Relay (hard to use in breadboards)
13 Shift Register (many wires)
14 Motor (small transistors and diodes)
15 LCD display (a favorite but many wires)
16 Simon Game (not included in our kits)

## Slide 55: Moving on...
build a computer from components
breadboards can get complex...but the skills they learn now might help in college!

## Slide 56: Sensors
Using AnalogRead() function to read values from 0 to 1023
https://www.arduino.cc/en/Reference/AnalogRead
Use map function to convert values into other ranges
newValue = map(inputValue, inLow, inHigh, outLow, outHigh)
Reads the value from the specified analog pin. The Arduino board contains a 6 channel (8 channels on the Mini and Nano, 16 on the Mega), 10-bit analog to digital converter. This means that it will map input voltages between 0 and 5 volts into integer values between 0 and 1023.
analogRead()

## Slide 57: All the light we can not see (and sounds we cannot hear)
Encourage students to use sensors that sense "invisible" information
Infrared and Ultrasound

## Slide 58: Best Practice Sensors
PIR Motion Sensor (Passive Infrared)
$1.40
http://www.ebay.com/itm/HC-SR501-Adjust-IR-Pyroelectric-Infrared-PIR-Motion-Sensor-Detector-Module-NEW/271638488228
PING Sensor (Ultrasonic distance sensor)
$1.00
http://www.ebay.com/itm/1pcs-Ultrasonic-Module-HC-SR04-Distance-Measuring-Transducer-Sensor-for-Arduino-/171983646391

## Slide 59: Not all are real "sensors" but all can be fun
KY-001 Temperature sensor module
KY-002 Vibration switch module
KY-003 Hall magnetic sensor module
KY-004 Key switch module
KY-005 Infrared emission sensor module
KY-006 Small passive buzzer module
KY-008 Laser sensor module
KY-009 3-color full-color LED SMD modules
KY-010 Optical broken module
KY-011 2-color LED module
KY-012 Active buzzer module
KY-013 Temperature sensor module
KY-015 Temperature and humidity sensor module
KY-016 3-color LED module
KY-017 Mercury open optical module
KY-018 Photo resistor module
KY-019 5V relay module
KY-020 Tilt switch module
KY-021 Mini magnetic reed modules
KY-022 Infrared sensor receiver module
KY-023 XY-axis joystick module
KY-024 Linear magnetic Hall sensors
KY-025 Reed module
KY-026 Flame sensor module
KY-027 Magic light cup module
KY-028 Temperature sensor module
KY-029 Yin Yi 2-color LED module 3MM
KY-031 Sensor module
KY-032 Obstacle avoidance sensor module
KY-033 Hunt sensor module
KY-034 Automatic flashing colorful LED module
KY-035 Class Bihor magnetic sensor
KY-036 Metal touch sensor module
KY-037 Sensitive microphone sensor module
KY-038 Microphone sound sensor module
KY-039 Detect the heartbeat module
KY-040 Rotary encoder module

## Slide 60: Success Stories
LED Costume Kit ($13.5)
Done with the Internet of Things Hackfest
LED Strip Box (Moving Rainbow)
Motor Controllers
Simple kit to move a motor forward and reverse
CoderDojo Robot
Done as advanced projects for CoderDojo students

## Slide 61: Sample Beginner Projects
Nightlight (photosensor and LED)
Room Alarm (PIR sensor and buzzer)
Temperature display and alarm
Tilt sensor and alarm
Simple Simon pattern replay game (4 push buttons, LEDs and optional speaker)
Motor controller

## Slide 62: Challenges
PC Can't Connect Using Thonny
(Upload will not work)
Drivers not installing
Mac unsigned drivers
Programs will not compile
Syntax errors

## Slide 63: Windows Device Manager
Note COM23 is the port

## Slide 64: Problem uploading to board
Note the Processor and Port

## Slide 65: Checking the USB on The Mac
About This Mac…
System Report…
USB

## Slide 66: Problem: The Rote Learner Problem
Students carefully follow the detailed steps in SparkFun inventor's kit guide
Each wire is carefully connected and checked
Each lab "works"
Students have little understanding of what is really going on and can't build their own projects

## Slide 67: Key Computer Science Topics
Variables
Loops (for loops)
Conditional statements (if/then/else)
Data types (integer, float, bytes)
Data range conversions

## Slide 68: Teach debugging
Learn how to add "print" statements
Open the serial monitor

## Slide 69: Addressable LED Strips (WS2812B)
1 Meter @$14.24
60 RGB LEDs/meter
$4.60 per LED strip
Easy to connect
  Ground wire
  5V power wire
  data wire

## Slide 70: Moving Rainbow Labs
Focus on fun colors and patterns
Reinforce many Computer Science concepts (loops, conditionals)
Perfect for costumes and interactive art
Online book with instructor's guide
  http://moving-rainbow.readthedocs.org/en/latest/README/
Simple to connect
(three wires)

## Slide 71: Controlling Motors: The H-Bridge Circuit
Close Switch 1 and 4 for forward direction
Closes switch 2 and 3 for reverse direction
Never close S1 and S2 or S3 and S4 together (short circuit)

## Slide 72: Motor Driver Labs
Based on standard low cost two motor controller chip (L293D) 40 cents each
Goal - make two motors turn forward and backward
Basis for robot movement
Once students believe they can control two wheels they are ready to build a simple robot
Over 75% of students that finish the motor driver lab go on to build their own robot!
http://www.ebay.com/itm/10Pcs-L293D-L293-Push-Pull-Four-Channel-Motor-Driver-IC-/140832908826

## Slide 73: Simple hookup
Introduction to "PWM" for motor speed control
H-Bridge circuit
Direction control
Use a potentiometers to change the direction and speed of two motors.

## Slide 74: 12 Volt battery to pin 8
Pin 8
5 Volts

## Slide 75: CoderDojo Robot Labs
Collision avoidance robot
Designed as advanced labs for CoderDojo students
Students use kits at CoderDojo and then purchase their own for around $35
Totally open design
  3 breadboards on the top
  Easy to change and add sensors
Includes addressable strip
Uses Arduino Nano

## Slide 76: Keep the steps small
Don't add too much complexity too fast
Blink
Analog
Breadboarding
Uploading
Blink
Sensors
Bluetooth
Wireless
Internet of Things
Raspberry Pi
UNIX
Wifi LAB
Servo

## Slide 77: MicroPython Kits
Basic Electronics kits - breadboarding basics $5/kits
Basic MicroPython kits - $25-$110 /kits
LED kits - $10 to $40
Robot kits - $40 to $300

## Slide 78: Sample Breadboard Kit
400 tie breadboard ($1.20)
Battery case or wall-transformer ($2-$4)
Jumpers (< $1)
10 Resistors (< 50 cents)
10 LEDs (< $1)
Optional Motor (< $2)
Optional Potentiometer (< $1)
No Raspberry Pi needed! No PC Needed!
Builds the foundation for all future Arduino labs
Help students build fine-motor skills
Easy to setup
Some soldering required for motors
Google: "Breadboard starter kit"
http://www.ebay.com/itm/BreadBoard-Starter-Kit-Power-Supply-Module-Resistors-Wires-more-/171924251290
Sample $25 Kit
Sample $10 Kit

## Slide 79: Sample $15 Kit
http://www.ebay.com/itm/Basic-Electronic-Component-Kits-Breadboard-Resistors-Power-Supply-Module-J0JF/141832343887
$15.00 US with shipping from China
Use to teach basics of breadboarding, power, conductivity, resistors, LEDs, potentiometers, and buttons
Excellent preparation for Arduino labs

## Slide 80: Sample item on e-Bay
Note to select "Buy It Now" and Sort by "Price + Shipping: lowest first"

## Slide 81: Breadboard vs. Little Bits
LEDs with resistors QTY 100 for $2.00 (2 cents each) but requires fine motor skills
Little Bits sells a Single LED for $10.00. Great for students that don't yet have fine motor skills...but does not teach breadboarding/debugging skills.

## Slide 82: SparkFun Inventor's Kit
Used in many CoderDojo labs
Many Arduino mentors now familiar with these kits
Good selection of parts and excellent printed guidebook
Redboard Version 3.2 list price is $99.00
  (Add $10 for Genuine Arduino from Italy)
No soldering required to use base kit
Soldering is used to reinforce and repair motors
Small parts moved to a separate bin

## Slide 83: SIK Guide and Case
SIK Guide and Case and reinforced cable ties on motors

## Slide 84: 16hertz Kits
Great value! $25.00
Requires 20 minutes of soldering for each kit
Larger servo, relay
Well written guide
http://www.16hertz.com/product/16hertz-uno-r3-beginner-kit-arduino-compatible/

## Slide 85: 37 Sensors Kit
http://www.ebay.com/itm/Pro-Compatible-37-in-1-Sensor-Modules-Kit-Arduino-Ultimate-MCU-User-Free-Case-/141772914818
37 Sensors for $27.00
Variety of devices (not all sensors) for under $1/device
Kit comes with no instructions and the contents frequently change
Many examples of how to use each device on the Internet
Remove any "mercury" switches

## Slide 86: Robot Kit
Open design
$35 in parts
Ping sensor on mini-breadboard to detect objects in front
Arduino Nano on a breadboard
LED strip
L293D Motor Driver
https://www.gitbook.com/book/dmccreary/coderdojo-robots/details

## Slide 87: Robots: mBot, MIP, Gizmo
Cozmo - $179.00
Coder MIP - $79.00
mBot - $99.00

## Slide 88: MicroCenter
Carry in-house brand Arduino for $9.99
Large selection of kits and sensors
2-3 times eBay "best prices"

## Slide 89: Encourage Volunteers
There are many parents that may have some programming or electrical knowledge
Find a parent or mentor to solder broken parts and put solid wire pins on components that are hard for small fingers
10 kits - no working motors
2 hours of soldering - 10 working motors
http://datadictionary.blogspot.com/2014/10/motors-for-arduino-labs.html

## Slide 90: Watch how students make "connections"
Have plenty of 22 gauge solid wire, jumper wires of various lengths
Add heat shrink around ends

## Slide 91: Mentors are critical for overcoming frustration
Problem
  Many kids hit "the wall" when they can't get a project to work
  New students can easily get frustrated and quit
  Parents purchase expensive Arduino kits and they go unused
The Solution: develop mentor programs
  Try CoderDojoTC (every other Saturday at the U of M)
  Keep students from thinking that Arduino is frustrating
  A good mentor will keep challenging the students

## Slide 92: Student / Book / Box / Mentor Relationship Analysis
Focus analysis on the six key relationships and the break/fix cycle
Student
Book or
Web Site
Robot/Kit
Teacher/Mentor

## Slide 93: Component/Libraries/Documentation/Sample Code
Where should we look for components? Have we used this component before? How many will we need for a classroom? Can I find other teachers that can help us get started?
Higher cost components with good documentation, libraries, examples and support. (Adafruit, Sparkfun)
Lower cost components with no documentation, no support and no sample code. (Amazon, e-Bay)

## Slide 94: Three Take-home Points
Always have a mentor
Studies show that spending two hours every other week keeps students on the STEM track
Ask students bring their ideas
The mentor's job is to find out how to make it happen
Work in teams to build concrete projects
"Social Constructionism" is perhaps the best way to learn both hard and soft skills

## Slide 95: Summary
Arduino is a foundation technology
Arduinos open many doors
Learning Arduino is great ways to help students become "makers" and become involved in project-based learning
Arduinos take time to master
Start simple
Purchase basic kits
Work with peers to help overcome problems
Come to CoderDojo to learn new things!

## Slide 96: Questions
Dan McCreary
dan.mccreary@gmail.com
https://github.com/dmccreary/moving-rainbow
https://github.com/dmccreary/coderdojo-robots
LinkedIn: https://www.linkedin.com/in/danmccreary/
Twitter: @dmccreary